### ESP32 Pin Mapping and Purpose
Pin Number	Label	Connected Component	Purpose
1	VDDA	Power	Analog power supply pin for the ESP32.
2	LNA_IN	Antenna	Connected to the onboard RF antenna for Wi-Fi communication.
3	VDD3P3	Power	3.3V power supply pin for internal RF and analog modules.
4	VDD3P3	Power	Another 3.3V power supply pin.
5	SENSOR_VP	GPIO	Connected to the ADC or analog sensor input.
6	SENSOR_CAPN	GPIO	Can be used for ADC input or capacitive touch sensing.
7	SENSOR_CAPP	GPIO	Can be used for ADC input or capacitive touch sensing.
8	SENSOR_VN	GPIO	Analog signal or ADC input.
9	CHIP_PU	Power Control	Power up pin for the ESP32; must be held high for normal operation.
10	FPGA_DONE_ESP	GPIO	Connected to the FPGA DONE pin to monitor the FPGA's configuration status.
11	ESP_FPGA_TYPE	GPIO	Pull-up or pull-down resistor to distinguish FPGA type (Artix-7 XC7S15 or XC7S25).
12	ESP_SDA_A4	GPIO	Typically used for I2C communication (SDA line).
13	32K_XN	GPIO or Clock	External 32.768 kHz crystal oscillator (negative terminal).
14	GPIO25	FPGA_PROGRAM_ESP	Used to reset or program the FPGA (connected to the PROG_B pin).
15	GPIO26	FPGA_INTB_ESP	Interrupt signal line for FPGA communication.
16	GPIO27	FPGA_CONFIG_DIN_ESP	Configuration data input for the FPGA during bitstream loading.
17	GPIO17	SD_CARD_WP (Write Protect)	Detects the write-protect status of the SD card.
18	GPIO16	SD_CARD_CD (Card Detect)	Detects whether an SD card is inserted.
19	VDD3P3_RTC	Power	3.3V supply pin for RTC (Real-Time Clock).
20	MTDI	JTAG or GPIO	GPIO or used for JTAG programming/debugging.
21	MTCK	JTAG or GPIO	GPIO or used for JTAG programming/debugging.
22	MTDO	JTAG or GPIO	GPIO or used for JTAG programming/debugging.
23	MTMS	JTAG or GPIO	GPIO or used for JTAG programming/debugging.
24	GPIO4	General Purpose I/O	Can be used for generic GPIO functionality.
25	GPIO16	SD_CARD_CD (Card Detect)	Connected to the SD card slot to detect the presence of an SD card.
26	GPIO17	SD_CARD_WP (Write Protect)	Connected to the SD card slot to detect write protection status.
27	GPIO27	FPGA_CCLK_ESP	Provides a clock signal to the FPGA during configuration.
28	GPIO28	FLASH_SHD	Flash memory pin.
29	GPIO29	FLASH_SWP	Flash memory write protect.
30	GPIO30	FPGA_CS	SPI Chip Select (for FPGA SPI communication).
31	GPIO31	FPGA_SCLK	SPI clock signal for communication with the FPGA.
32	GPIO32	FPGA_MOSI	SPI data output (Master Out, Slave In) to FPGA.
33	GPIO33	FPGA_MISO	SPI data input (Master In, Slave Out) from FPGA.
34	GPIO18	ESP_QSPI_CLK	QSPI clock signal for accessing flash memory.
35	GPIO23	ESP_QSPI_D	QSPI data signal.
36	GPIO5	ESP_QSPI_CS	QSPI chip select signal.
37	GPIO21	General Purpose I/O	GPIO for custom tasks or I2C functionality (SCL).
38	GPIO19	UART_TX	UART Transmit (for USB communication or debugging).
39	GPIO22	UART_RX	UART Receive (for USB communication or debugging).

### Notes and Key Features
1. Programming Pins for FPGA:
  1. GPIO25, GPIO26, GPIO27, and GPIO21: These are directly involved in the FPGA programming sequence (PROG_B, CCLK, DATA0, and DONE).
2. SPI Communication:
  1. SPI communication between ESP32 and FPGA is handled by GPIO30 (CS), GPIO31 (SCLK), GPIO32 (MOSI), and GPIO33 (MISO).
3. SD Card Pins:
  1. GPIO16 and GPIO17: Monitor the presence of an SD card and its write-protect status.
4. General GPIO Pins:
  1. The remaining GPIO pins can be repurposed for custom tasks or additional interfaces (I2C, UART, etc.).
5. UART and USB Communication:
  1. GPIO19 and GPIO22: Connected to the USB-to-UART bridge for PC communication via a USB cable.